## Slide 1: River Modeling
Segmentation and Model Resolution
Finite Segment Method

## Slide 2: 3.1 Segmentation and Model Resolution
Segmentation = process of dividing space and matter into increments;
Space: a water body can be  into volumes;
For which mass balance equations are written.
1
2
3
4
5
6
7
… n

## Slide 3: 3.1 Segmentation and Model Resolution
Volume: matter may be  into different chemical and biological forms;
For which separate eqns would be written;
n segments + m substances = m  n mass balance eqns.

## Slide 4: 3.1 Segmentation and Model Resolution
Aside from space and matter, there is a temporal aspect to segmentation;
Related to the fact that mass balance defines changes in water body over a finite period of time;
Model describes additional spatial and material detail by using more segments;
 temporal focus: shorter “finite period” or time step for mass balance computation;
Model resolution: degree to which space, time and matter are segmented.

## Slide 5: Model Resolution
 photography (Camera’s lens focus);
At times the foreground is important;
At other times distant details might be of interest.

## Slide 6: Significance of Model Resolution for WQ analysis
Two basic ways:
  Fine-scale phenomenon may have a direct, causative influence on predictions made on the coarser scale;
  Influence of the problem context on the choice of scales.

## Slide 7: 1. Fine scale  Coarse scale phenomenon
Primarily a function of substance’s properties and physical characteristics of the system;
E.g. certain pollutants (e.g. enteric bacteria) die rapidly upon entering a water body;
 typically at  levels near sewage discharge;
 rapidly  background levels in open waters;
Near-shore model of bacterial pollution;
Require relatively fine spatial and temporal segmentation around sewage outfalls.

## Slide 8: 1. Fine scale  Coarse scale phenomenon
Chart: x (m)
| 0 | 5 | 10 | 15 | 20 | 25
k = 0.75 /m | -1 | -1 | -1 | -1 | -1 | -1
k = 0.25 /m | 1 | 0.2865 | 0.082085 | 0.023518 | 0.0067379 | 0.0019305
k =0.75/m | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
Chart: x (m)
| 0 | 5 | 10 | 15 | 20 | 25
k = 0.75 /m | 1 | 0.023518 | 0.00055308 | 1.3007e-05 | 3.059e-07 | 7.1941e-09
k = 0.25 /m | 1 | 0.2865 | 0.082085 | 0.023518 | 0.0067379 | 0.0019305
k =0.75/m | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
Chart: x (m)
| 0 | 5 | 10 | 15 | 20 | 25
k = 0.75 /m | 1 | 0.023518 | 0.00055308 | 1.3007e-05 | 3.059e-07 | 7.1941e-09
k = 0.25 /m | 1 | 0.2865 | 0.082085 | 0.023518 | 0.0067379 | 0.0019305
k =0.75/m | 1 | 0.47237 | 0.22313 | 0.1054 | 0.049787 | 0.023518 | 0.00055308 | 1.3007e-05 | 3.059e-07
C  slowly
C  rapidly
Require finer spatial segmentation, particularly near release point

## Slide 9: 1. Fine scale  Coarse scale phenomenon
Conservative or slowly reacting substances;
Often can be modelled with coarser schemes;
That treat the whole water body as a single well-mixed segment;
Physical chars dictate segmentation level;
E.g. dendritic lakes - 1 segment unrealistic;
Eutrophication - thermal stratification;
  Need multiple vertical.

## Slide 10: 2. Influence of prob context on choice of scales
E.g. phytoplankton go through growth cycles on seasonal time scales and exhibit patchiness on small space scales.
Steady
Seasonal
Monthly
Daily/Hourly

## Slide 11: 2. Influence of prob context on choice of scales
But WQ planner might not have the funds to develop models to simulate such short-term variability;
Often occur when large numbers of small lakes were being evaluated.

## Slide 12: 2. Influence of prob context on choice of scales
Spatial and temporal aggregation results in negligible loss of relevant planning info;
Opt for a coarser scale model;
Bacterial contamination of beaches;
Finer scale approach is necessary;
To handle the problem effectively.

## Slide 13: 3.1 Segmentation and Model Resolution
Temporal, spatial and kinetic scales of a problem often are interrelated;
Fast kinetic processes, e.g. jet mixing of thermal effluents or bacterial die-off ;
Tend to manifest themselves on local (i.e. small) time and space scales;
Problems with slow reactions, e.g. decay of persistent contaminants;
Important on whole-system, long-term basis.

## Slide 14: 3.2 Finite Segment Method
Water body is often  into a series of computational elements called segments;
To account for variations over the water body;
Levels of substances at various locations;
3
1
4
2
5
8
7
6
10
9

## Slide 15: 3.2 Finite Segment Method
Best not to have too many segments than necessary;
Imply a greater level of detail than is generally possible to parameterize;
Greater opportunity for error (modify param);
Comp. less efficient;
Calibration difficult.

## Slide 16: Segmentation Considerations
Spatial scale of the problem
  Segment of a water body (e.g., reach, embayment)
  Whole water body (e.g., main river, lake, estuary)
  Whole river basin network

## Slide 17: Segmentation Considerations
Dimensionality and spatial discretization of segments
  Box, 1-, 2-, 3-dimensions
  Horizontal: tens of meters to tens of kilometers
  Vertical: whole water column to tens of cm;

## Slide 18: Segmentation Considerations
Physical components
  Water column (epilimnion, hypolimnion)
  Benthic sediments (surface, subsurface)
Model limitations
  Maximum # of Segments 3000
  Maximum # of Time Pairs 4000

## Slide 19: Segmentation Considerations
  Network scale determines how precisely the model will be able to reproduce observed gradients.

## Slide 20: 3.2 Finite Segment Method
FSM - segmentation of model ecosystems;
Into various “completely mixed” boxes;
Of known volume and interchange;
Process known as compartmentalization;
Popular assumption in fate modelling;
Because assumption of complete mixing;
Reduces the set of PDEs (in time and space);
To one of ODEs (in time only).

## Slide 21: 3.2 Finite Segment Method
Nevertheless, it is possible to recover some coarse spatial information;
By introducing a number of interconnected segments/compartments;
Interchange between segments is simulated via bulk dispersion or equal counterflows between segments.
1
2
4
5
6
7
8
11
10
9
3

## Slide 22: 3.2 Finite Segment Method
Figure 3.1 Simple representation of an estuary with finite segments
Estuary width gradually  towards sea;
Laterally and vertically well-mixed;
Concentration gradient along the x-axis.

## Slide 23: 3.2 Finite Segment Method
A substance reaction in a water body is important aspect of the substance’s fate in the environment;
But an equally important process has to do with the rate of a substance’s transport in the aquatic environment;
A substance is transported by water movement and may undergo additional transport processes such as decay or sedimentation.

## Slide 24: Transport Processes
Decay – substance reduced in mass due to decomposition or sedimentation;
Advection – sub movement at current velocity;

## Slide 25: Diffusion and Dispersion
Diffusion: process where a constituent moves from a higher concentration to a lower concentration.
Dispersion:
  process by which substance is mixed within water column.
  mixing caused by physical processes.
time

## Slide 26: Dispersion
3 processes contribute to mixing (dispersion):
  Molecular diffusion,
  Turbulent diffusion, and
  Dispersion.
Random motion of particles
Turbulent mixing of particles
Mixing caused by variations in velocities

## Slide 27: 1. Molecular diffusion
Mixing of dissolved substances;
Due to random walk of molecules within fluid;
Caused by kinetic energies of molecular vibrational, rotational and translational motion;
In essence, molecular diffusion corresponds to an increase in entropy;
Move from regions of high concentration to regions of low concentration;
According to Fick’s laws of diffusion.

## Slide 28: 1. Molecular diffusion
Generally not an important process;
In the transport of dissolved substances in natural waters;
Except relating to transport through thin and stagnant films ;
At the air-water interface or transport through sediment pore water.

## Slide 29: 2. Turbulent diffusion
@ Eddy diffusion;
Mixing of dissolved substances caused by microscale turbulence;
Advective process at microscale level caused by eddy fluctuations in turbulent shear flow;
Shear forces within the body of water are sufficient to cause this form of mixing;
Several orders of magnitude > mol. diffusion;
A contributing factor in dispersion.

## Slide 30: 3. Dispersion
Interaction of turbulent diffusion with velocity gradients;
Caused by shear forces in the water body;
Greater degree of mixing known as dispersion;
Transport of substances in streams and rivers;
Is predominantly by advection;
But transport in lakes and estuaries is often dispersion-controlled.

## Slide 31: Mathematical Representations
Diffusion:
  Fick’s First Law of Diffusion
Dispersion:
  Analogous to Fick’s First Law

## Slide 32: Range of Values for Dispersion
Process | Direction | Typical Range [m2/s]
Molecular Diffusion | Vertical | 10-8 to 10-9
 | Lateral | 10-8 to 10-9
 | Longitudinal | 10-8 to 10-9
Turbulent Diffusion | Vertical | 10-6 to 10-2
 | Lateral | 10-2 to 102
 | Longitudinal | 10-2 to 102
Dispersion | Vertical | 10-3 to 10-1
 | Lateral | 10-2 to 100
 | Longitudinal | 10-1 to 104

## Slide 33: Dispersion Coefficients
Condition | Dispersion Coefficient [m2/s]
Molecular Diffusion | 10-9
Compacted Sediment | 10-11 to 10-9
Bioturbated Sediment | 10-9 to 10-8
Lakes – Vertically | 10-6 to 10-4
Large Rivers – Lateral | 10-4 to 10-3
Large Rivers – Longitudinal | 100 to 102
Estuaries – Longitudinal | 102 to 103

## Slide 34: Dispersion

## Slide 35: Dispersion + Advection

## Slide 36: 3.2 Finite Segment Method
 mass balance equation at ith segment is influenced by four components;
transport of the substance s by current of the water (advective flow);
transport of the substance s due to mixing within the water body (dispersion);
loss of mass due to decay process;
source of substance s.

## Slide 37: 3.2 Finite Segment Method
 mass balance equation at ith segment is influenced by four components;
transport of the substance s by current of the water (advective flow);
transport of due to mixing within the water body (dispersion);
loss of mass due to decay process;
source of substance s.

## Slide 38: 3.2 Finite Segment Method

## Slide 39: (i) Advective Flow
Mass per unit time for s that enters and exits segment i due to advective flow Q m3/s;
Input of mass kg/s from upstream segment:
(3.1)

## Slide 40: (i) Advective Flow
Transport of mass by advective flow that exits segment i:
(3.2)

## Slide 41: (ii) Dispersion
Mass change due to diffusion and mixing;
Transport directly proportional to mass conc difference between two adjacent segments;
Exchange of mass between segment i and segment i – 1 due to dispersion:
(3.3)

## Slide 42: (ii) Dispersion
Exchange of mass between segment i and segment i + 1 due to dispersion:
(3.4)

## Slide 43: (ii) Dispersion
Si-1 > Si : mass from Seg i-1 to i;
Si > Si-1 : mass from Seg i to i-1;
Similarly for interface of Seg i and i+1;
Bulk dispersion coefficient is related to E:
(3.5)

## Slide 44: (ii) Dispersion
Ai-1, i m2 = CS area between Seg i and i-1;
m = mean length between Seg i and i-1;
(3.5)
Figure 3.3 Cross sectional area, mean length and segment length

## Slide 45: (iii) Decay
For mass loss due to first-order decay process:
with ki s-1 = decay coefficient of segment i.
Vi m3 = volume of segment i.
(3.6)

## Slide 46: (iv) Sources and Sinks
Source or sink of substance s:
(3.7)
+

## Slide 47: 3.2 Finite Segment Method
Total quantity of all masses obtained must;
= Rate of change in mass at segment i;
for with Vi constant;
Good approximation for most estuaries.
(3.8)

## Slide 48: Overall Mass Balance at Segment i
Si
Si-1
Si+1
(3.9)
Figure 3.2 Notations for segment i illustrating advective flow, dispersion, mixing and decay of substance s.

## Slide 49: 3.2 Finite Segment Method
Eqn (3.9) is a numerical approx of
(3.9)
(3.10)

## Slide 50: 3.2 Finite Segment Method
1st - order linear ODE, time-dependent;
Assume steady-state, i.e. input, flow, exchange and reaction rate do not change with time:
n segments  n number of Eqn (3.9).
 Eqn (3.9)
= linear algebraic eqn

## Slide 51: 3.2 Finite Segment Method

## Slide 52: 3.2 Finite Segment Method
Segment 1:
Su
S1
S2
…
(3.11)

## Slide 53: 3.2 Finite Segment Method
Segment n:
Sn-1
Sn
Sb
…
(3.12)

## Slide 54: 3.2 Finite Segment Method
Group to the left all terms with si-1, si, si+1;
(3.13)

## Slide 55: 3.2 Finite Segment Method
Let:
(3.14)
(3.15)
(3.16)
Eqn (3.13) can be simplified to
(3.17)

## Slide 56: 3.2 Finite Segment Method
Segment 1:
Su
S1
S2
…
(3.11)
(3.18)
(3.19)

## Slide 57: 3.2 Finite Segment Method
Segment n:
Sn-1
Sn
Sb
…
(3.12)
(3.20)
(3.21)

## Slide 58: 3.2 Finite Segment Method
(3.22)
 The complete set of eqns for n segments:

## Slide 59: 3.2 Finite Segment Method
(3.23)
In matrix form:

## Slide 60: 3.2 Finite Segment Method
(3.23) : Boundary value problem-steady-state;
Boundary conditions: su and sb;
FSM – can only be solved easily by hand;
For systems of dimension 3 by 3;
River pollution - complex matter;
Requires division of river into many segments;
For more accurate and reliable solution.
 system of equations with high dimensions;
Numerical method - I1DISP (Koh, 2004).

## Slide 61: I1DISP – Steady-state Model

## Slide 62: 3.2 Finite Segment Method
Non steady-state, ds/dt  0;
Initial condition;
Initial value problem;
Runge Kutta methods;
E1DISP.

## Slide 63: Example 3.1
Consider a uniform river with cross sectional area A = 20 m2, length L = 3000 m, velocity u = 0.1 m/s and dispersion coefficient E = 0.0 m2/s. This river is divided into three uniform segments with x = 1000 m for each segment.

## Slide 64: Example 3.1
A chemical is released into segment 1 of the river at the rate of W = 0.1 kg s-1. This chemical decays at the rate of k = 10-4 s-1. The water at the upstream and downstream segments is assumed to have a chemical concentration of 0.0 kg m-3.
Find the concentration for every segment c1, c2, c3 after the steady state is achieved.

## Slide 65: Example 3.1
A = 20 m2 L = 3000 m u = 0.1 m/s
E = 0.0 m2/s x = 1000 m W = 0.1 kg/s
k = 10-4 s-1

## Slide 66: Example 3.1

## Slide 67: Example 3.1

## Slide 68: Example 3.2
Consider a uniform river with cross sectional area A = 20 m2, length L = 3000 m, velocity u = 0.1 m/s and dispersion coefficient E = 0.2 m2/s. This river is divided into three uniform segments with x = 1000 m for each segment.

## Slide 69: Example 3.2
A chemical is released into segment 1 of the river at the rate of W = 0.1 kg s-1. This chemical decays at the rate of k = 10-4 s-1. The water at the upstream and downstream segments is assumed to have a chemical concentration of 0.0 kg m-3.
Find the concentration for every segment c1, c2, c3 after the steady state is achieved.

## Slide 70: Example 3.2
A = 20 m2 L = 3000 m u = 0.1 m/s
E = 0.2 m2/s x = 1000 m W = 0.1 kg/s
k = 10-4 s-1

## Slide 71
Example 3.2 - Solution

## Slide 72
Examples 3.1 & 3.2: Comparison
Chart: x (m)
| 0 | 1000 | 2000 | 3000 | 4000
E = 0.0 m2/s | 0 | 25 | 12.5 | 6.25 | 0
E = 0.2 m2/s | 0 | 24.96 | 12.49 | 6.24 | 0
c (mg/L) | x (m) |  |  |  | 
 | 0 | 1000 | 2000 | 3000 | 4000
Example 3.1 | 0 | 25 | 12.5 | 6.25 | 0
Example 3.2 | 0 | 24.96 | 12.49 | 6.24 | 0

## Slide 73: Example 3.3
A = 20 m2 L = 3000 m u = 0.1 m/s
E = 0.0 m2/s x = 1000 m W = 0.1 kg/s
k = 10-4 s-1

## Slide 74
Example 3.3 - Solution

## Slide 75: 2D Water Quality

## Slide 76
Thank You